SMART TWO WHEELER ACCIDENT DETECTION

Vega IoTv2 Processor

- https://vegaprocessors.in/devboards/ariesiot.php
- VEGA ET1031 Microprocessor
- THEJAS32 SoC
- This board is a development platform based on THEJAS32 ASIC which operates at a frequency of 100MHz. THEJAS32 SoC includes VEGA ET1031 Microprocessor, 256KB internal SRAM, Three UARTs, Four SPIs, Three TIMERs, Eight PWMs, Three I2C interface, 32 GPIOs etc.

>> Data Sheet
https://vegaprocessors.in/files/ARIES_IoT_V2.0_DATASHEET.pdf

>> BMI088 Sensor
- https://www.bosch-sensortec.com/media/boschsensortec/downloads/datasheets/bst-bmi088-ds001.pdf
- By BOSCH
- BMI088 is an inertial measurement unit (IMU) for the detection of movements and rotations in 6 degrees of freedom (6DoF). It combines the functionality of two inertial sensors in one device: an advanced triaxial 16-bit gyroscope and a versatile, leading-edge triaxial 16-bit accelerometer.
- For optimum system integration, BMI088 is fitted with digital interfaces (SPI or I2C), offering a wide VDDIO voltage range from 1.2V to 3.6V
- Block Diagram is in pg.no. 13
- High Resolution: 16-bit digital resolution for both the accelerometer and gyroscope.
- Measurement Range: The accelerometer has a range of ±3g, ±6g, ±12g, and ±24g, while the gyroscope has a range of ±125°/s to ±2000°/s

>> NEO6M GPS Module
https://content.u-blox.com/sites/default/files/products/documents/NEO-6_DataSheet_%28GPS.G6-HW-09005%29.pdf
- TX of NEO6M - GPIO-4 of Processor and RX-GPIO-3
- For NEO6M GPS Module communication, we did not use the UART comminication, rather we used Software-based serial communication using SoftwareSerial library, which enables serial communication on other digital pins of an Arduino board, beyond the default hardware serial ports

>> Buzzer
Pin.75 (GPIO.2 - 11) => PWM(7) Pulse Width Modulation.

>> A basic reference code
#include <SPI.h>

#include <SoftwareSerial.h>

#include "BMI088.h"
#define VEGA_ARIES_IOT_V2
#define buzzer 7 //buzzer connected to PWM pin 7
#define period 500

SoftwareSerial ss(4, 3); //TX-GPIO-4 and RX-GPIO-3

SPIClass SPI(2);

/* accel object */
Bmi088Accel accel(SPI,0xFF);
/* gyro object */
Bmi088Gyro gyro(SPI,21);

void setup()
{
  int status;

  /* USB Serial to print data */
  Serial.begin(9600);

  while(!Serial) {}

  /* start the sensors */
  status = accel.begin();
  ss.begin(9600);

  if (status < 0) {
    Serial.println("Accel Initialization Error");
    Serial.println(status);
    while (1) {}
  }
}

void loop()
{
  #if defined (VEGA_ARIES_IOT_V2)

  /* read the accel */
  accel.readSensor();

  /* print the data */
  float accely = accel.getAccelY_mss();

  Serial.print("X_axis = ");
  Serial.print(accel.getAccelX_mss());
  Serial.println();

  Serial.print("Y_axis = ");
  Serial.print(accel.getAccelY_mss());
  Serial.println();

  Serial.print("Z_axis = ");
  Serial.print(accel.getAccelZ_mss());
  Serial.println();

  if (accely > 7)
  {
    while (ss.available() > 0){
    // get the byte data from the GPS
    tone(buzzer,period);
    byte gpsData = ss.read();
    Serial.write(gpsData);
  }
  }

  #else
  Serial.println("Choose the correct board! " );
  #endif
}